## Slide 1: VSMI to Mitigate Infection Risks
Roy Vasher, Purdue-WHIN Education Consultant

## Slide 2: What is VSMI?
VSMI is an acronym for Value Stream Mapping plus Infection risk mitigation.
The VSM methodology was initially used by Toyota to eliminate waste and is now a vital tool that is used by Lean practitioners everywhere.
A VSMI map provides a visual representation across the plant floor to enable you to identify potential areas of Infection risk

## Slide 3: VSM Material and Process Flow Map – Logical View
Factory Operations
Shipping
INV
Receiving
INV
Cutting
Notch
Form
Weld
Buff
NVA
VA
4 hr.
1 day
5 min
2 min
2 min
2 min
2 min
Types of Waste
Transportation
Inventory
Motion
Waiting
Over Production
Over Processing
Defects
New Concern
Infection Risk

## Slide 4: Factory Floor Flow – Aerial View – Prior Mitigation
Aisle
Aisle
Receiving
Shipping
Cutting
Notch
Form
Weld
Buff
Steel
Less than 6 Ft
Less than 6 Ft
Supervisor
Mobile worker
Two-way aisle way

## Slide 5: Factory Floor Flow – Aerial View – With Mitigation
Aisle
Aisle
Receiving
Shipping
Cutting
Notch
Form
Weld
Buff
Steel
Move Worker
Aisle
One-Way
One-Way
Supervisor
Make aisles one-way
Wear Sensor
Sensor to Quarantine incoming parts

## Slide 6: Next VSMI Step
CAD* Software Model
  Use a CAD type software to translate the VSM logical flow into an aerial view of the factory floor using actual dimensions of floor plan as well as machines and workstations.
  CAD software can be used to create a 3D view and used to simulate relocation of machines and workstations
  Also, analyze traffic floor around the factory floor and redesign flow to keep workers separated by 6 feet when walking around – for example create one-way routes and either side of the wide aisles.
VISIO
  If you do not have access to CAD, the next best option is to use VISIO
Computer Aided Design

## Slide 7: Actual Company Example Focus Area - Fabrication
VSMI
38’ x 44’ area
.00479 personnel/sq. ft density
Operators work close to one another
High traffic volume for small area
Before
After

## Slide 8: Future Opportunity
Short-term: Introduction of Infection Mitigation may have a negative impact on being “Lean” or efficient
Future: Redesign the factory to not only be safe but more efficient by strategic adoption of smart technology

## Slide 9: Example of AI Driven Solutions for VSMI
Video Analytics at Purdue
  To create scans to enable creation of accurate Factory Floor Plan
Robotic Dogs at Ford
  To create 3D scans to enable creation of accurate Factory Floor Plan
  https://mashable.com/video/ford-boston-dynamics-robot-dog/

## Slide 10
Robotic Dogs at Ford

## Slide 11: VSMI to Mitigate Infection Risks The end
Roy Vasher